Radio controlled step Movement with Chime

Instruction Manual

- Automatic time setting

Insert one AA Battery into the battery compartment. The hands will stay in the 12'o clock position and the clock will search for the DCF77 signal for 3 Minutes. (You can place the clock to the window for better reception of the signal.)

- If the reception of the DCF77 signal succeeds, the hands will be set automatically into the right time position and the clock will start running.

- If the reception of the DCF77 signal doesn't succeed, the clock will start running from the 12'o clock position. Try to remove the batteries and repeat the whole process again. If the reception of DCF77 signal doesn't succeed again, you can set the time manually.

- Manual time setting (M.SET button)

Hold the button M.SET for 3 Seconds. The minute hand starts running and when you push the button M.SET again, the minute hand moves by one minute forwards. If you don't push any button for 5 Seconds, the time setting will end and the clock starts running from the choosen position.

- Reset button

By pushing the reset button will be the clock set back to the factory settings (the same as after inserting the batteries). The clock stays in the 12'o clock position.

- REC button
Hold the REC button for 3 Seconds until the hands stand still. The clock will search for the DCF77 signal. Wait 3 Minutes until the automatic time setting begins.

- Chime-Box

The Chime-Box has its own power supply. After the time setting, insert 2 AA Batteries into the battery compartment (beside the clockwork).

!!!ATTENTION!!! Do not set the time by direct rotation of the clock hands. The clock will not work correctly.

| Icon | Function | Description |
| --- | --- | --- |
|  | OPT | Clock play music from 06.00AM to 22.00PM. It does not play music from 22.00PM to 06.00AM |
|  | Light sensor control | No light sensor function available. Off - no music will be played. |
|  | Shut | off |
|  | Volume control | 3 levels of loudness: 1)low / 2)normal / 3)loud |
|  | Music switch | 4 options: 1) Notre Damme + strike 2) Westminster + strike, 3)Westminster, 4)Clank |
| RESET | Reset switch | reset |
| SET | Play switch | Play music |

Chime-Box function definition

Notre Damme + strike: The clock will play music associated with Notre Damme every hour and strike. (It means that chime will strike five times at five o´clock.)

Westminster + strike: The clock will play music associated with Westminster Abbey every hour and strike. (It means that chime will strike five times at five o´clock.)

Westminster: The clock will play Westminster melody every hour.

Clank: It means that clock will strike every hour accordingly to current time (it will strike five times at five o´clock).

Used batteries: C / R14 /SUM-2 (AA Battery)

# Text boxes

Market supplier:

Jasněna Vláhová

Nové Město nad Metují

www.vlahova.cz